## Slide 1: Infineon Academy Distribution Training Mastering ModusToolbox™ in Your Development Workflow
Clark Jarvis – Software and Tools Product Marketer
April 2026

## Slide 2: Agenda
Working effectively with version control and git
1
Sharing, importing and exporting projects
2
Understanding the ModusToolbox™ BSP concept
3
Workflows to develop and utilize a custom BSP
4
Middleware integration with Library Manager and Makefiles
5
Introduction to the upcoming ModusToolbox™ SDK
6
Q&A
7

## Slide 3: Session Roadmap
# | Topic | Key Skill
1 | Version Control & Git | Know what to commit, what to ignore, how to collaborate
2 | Project Sharing & Export | Send a working project to anyone — colleague, customer, Infineon
3 | Understanding BSPs | How BSPs bridge your app code and hardware
4 | Custom BSP Workflows | Build a custom BSP for production hardware
5 | Middleware & Library Manager | Add libraries, manage dependencies, understand the Makefile
6 | The ModusToolbox™ SDK | What's coming and why it matters

## Slide 4: Working effectively with version control and git

## Slide 5: The ModusToolbox™ project structure

## Slide 6: The .mtb dependency model
Workspace clone of library
mtb_shared/retarget-io/release-v1.9.0/
Resolution of dependencies
make getlibs
User required library
deps/retarget-io.mtb
URL: https://github.com/Infineon/retarget-io
Version: release-v1.9.0
Path: libs/retarget-io
Parses the .mtb file
  Runs git clone with the specified URL and version tag
  Resolves transitive dependencies (each library can have its own deps/)
Generates
  libs/mtb.mk
  SEARCH_* paths
Full library source code, checked out at the pinned version.
Shared across all projects in the workspace.
  Never committed to any project's Git repo.

## Slide 7: What are deps/ and libs/ folders?
Text
What is inside .mtb files you declare
Who controls it You (the developer)
What is represents What you asked for
Version control Yes, this should in the git commit
What is inside resolved .mtb file or generated .mk files
Who controls it make getlibs (the tool)
What is represents Everything the build actually needs
Version control No, this is restored and reconstructed
VS
deps/
libs/

## Slide 8: What to commit, what to ignore?
ModusToolbox™ Code Example projects include a starting .gitignore reference file.
This file should be edited based on the user’s workflow
COMMIT | IGNORE
Makefile | build/
main.c and all source files | mtb_shared/ (regenerated by make getlibs)
deps/*.mtb | libs/ (transitive .mtb + mtb.mk pointing to mtb_shared)
bsps/ (BSP customizations) | .vscode/ (user-specific)
.gitignore itself | .cache/ (clangd / IntelliSense index)

## Slide 9: The version-controlled project flow
Clone the project
Resolve Dependencies
Import into IDE (optional)
Build
Working Binary
git clone <project-url>
Gets Makefile, main.c, deps/*.mtb, bsps/ — everything committed to Git
Open Eclipse IDE, VS Code, IAR Embedded Workbench, or Arm uVision
Follow specific steps from respective ModusToolbox™ IDE user guides
make getlibs (Importing into Eclipse or VS Code will complete this step)
Reads deps/*.mtb → clones libraries to mtb_shared/ → generates libs/mtb.mk
Build application with make build or via IDE
Compiles application + all dependencies into firmware binary
Flash to board with make program or via IDE

## Slide 10: Git workflow best practices
VS Code include built-in version control tracking, management, and visualization
Eclipse includes additional Views that support version control
ModusToolbox™ (on Windows) include a version of Cygwin Git
  This is what ModusToolbox™ uses by default
  This instance does use different git configurations
Practice | Why
One project per repo (preferred) | Clean history, independent versioning
Commit .mtb files | Reproducible dependency resolution
Never commit mtb_shared/ | It's regenerated; committing bloats the repo enormously
Tag releases | Match your project version to tested BSP/middleware versions
Document BSP + MTB version in README | e.g., "Tested with KIT_PSC3M5_EVK in ModusToolbox™ 3.7"
Use branches for BSP variants | If supporting multiple boards, branch per target

## Slide 11: Demo / Exercise Clone a real project and verify dependencies

## Slide 12: Exercise - Clone a real project and verify dependencies
Step | Command / Action | Expected Result
1 | Open Modus-Shell | 
2 | mkdir C:/MTB_Training && cd C:/MTB_Training | Create a workspace directory for the training
3 | git clone https://github.com/ClarkJ-Infineon/mtb-training-blinky | Project cloned into workspace (no mtb_shared/ or libs/ yet)
4 | cd mtb-training-blinky | 
5 | ls deps/ | See .mtb files for BSP and libraries
6 | make getlibs | Libraries cloned into ../mtb_shared/, libs/mtb.mk generated
7 | make build | Successful build for KIT_PSC3M5_EVK
8 | Inspect libs/ directory | See transitive .mtb files and mtb.mk with SEARCH paths
9 | Inspect libs/mtb.mk | See the SEARCH_ paths that wire libraries into the build

## Slide 13: Sharing, importing and exporting projects

## Slide 14: Three typical ways to share a project
Do not include mtb_shared/ in archives. mtb_shared/ is a workspace-level cache shared across all projects.
It contains every library version you've ever resolved, not just the ones your project uses.
Including it unnecessary files (often 200+ MB), creates confusion for the recipient, and may be overwritten anyway if the import process re-runs make getlibs.
Always let the recipient run make getlibs to get exactly what the project needs.
Scenario | Method | What controls the outcome | Includes mtb_shared?
Git repo (push/pull) | Cleanest for teams leveraging Git | .gitignore Defines what's tracked vs. excluded | No Recipient runs make getlibs
mtbarchive (CLI or GUI) | MTB-aware archive Includes the right files, excludes generated artifacts | Built-in best practices, tool knows the MTB project structure | No Recipient runs make getlibs
IDE Export / manual ZIP | IDE "Export ModusToolbox™ Application" or zip | User's understanding of what to include — YMMV | No See warning below

## Slide 15: ModusToolbox Archiving and Sharing Utility - mtbarchive
GUI version is accessible via
  Eclipse IDE for ModusToolbox™ Quick Panel
  VS Code ModusToolbox™ Assistant extension
  ModusToolbox™ tools installation directory
CLI version available from Modus-Shell
  mtbarchive -o my_project_archive.zip -f <project-folder>
Why use it over a plain ZIP?
  Knows which artifacts are generated vs. authored won't accidentally include 200 MB of libs/
  Produces a clean archive that recipients can open with make getlibs → make build
  Ideal for support tickets, customer handoff, email/USB sharing

## Slide 16: Saving and sharing your work with git
Working Directory
Staging Area
Remote Respository
Your local files
Edit freely here
Changes selected for next commit
Local Repository
Permanent history on your machine
GitHub / GitLab
Shared with team
# Check what's changed
git status
# Stage specific files (or all changes)
git add <file>
git add .
# Commit with a descriptive message
git commit -m "Add UART debug output to main loop"
# Push to remote repository
git push origin main
# Pull latest changes from remote
git pull origin main
git add
git commit
git pull
git push
Best Practices | Why
Commit often, in small logical chunks | Easier to review, revert, and bisect issues
Write descriptive commit messages | Future-you (and teammates) will thank you
Always make build before committing | Don't push broken code
Review git status before committing | Catch unintended files (e.g., build/ artifacts)

## Slide 17: Getting a shared project into your IDE
Eclipse IDE for ModusToolbox™:
  Clone or copy the project into your desired workspace folder
  Launch Eclipse IDE and set the workspace to the project's parent folder
  From the Quick Panel → click Import Existing Application In-Place
  Select the project folder → Eclipse registers it as a managed MTB project
VS Code (with ModusToolbox™ extension):
  Clone or copy the project to the desired location
  Open VS Code → File → Open Folder... → select the project folder
VS Code (without ModusToolbox™ extension):
  Clone or copy the project to the desired location
  Open Modus-Shell, navigate to the project folder
  Run make vscode — generates .vscode/ settings and a .code-workspace file
  Open the generated .code-workspace file in VS Code
IAR / µVision: Refer to the respective user guides, similar import-in-place workflow applies. Use make ewarm8 or make uvision5 from Modus-Shell to generate IDE project files.

## Slide 18: Demo / Exercise IDE import and archive / sharing export

## Slide 19: Exercise - IDE import and archive / sharing export
Step | Action | Expected Result
1 | Launch ModusToolbox™ Eclipse IDE | When prompted for workspace, set to C:/MTB_Training
2 | From the Quick Panel → Import ModusToolbox™ Application In-Place | Select mtb-training-blinky folder
3 | Project appears in Eclipse Project Explorer | Source files, BSP, and dependencies visible
4 | Build from Eclipse (Quick Panel → Build Application) | Confirm the project builds successfully in the IDE
5 | From Quick Panel → Tools section → launch ModusToolbox™ archiving and sharing | GUI opens with project pre-selected

## Slide 20: Understanding the ModusToolbox™ BSP concept

## Slide 21: What is a ModusToolbox™ BSP?
The BSP answers three questions:
  Which chip — device ID, core type, flash/RAM sizes
  How is it wired — pin assignments, crystal frequencies, debug interface
  How does it boot — startup code, linker scripts, memory map
Silicon (MCU)
Middleware / Peripheral Drivers
Your Application Code
Device-family API layer
PSOC™ Control, PSOC™ Edge, etc…
Portable across boards
Pins, clocks, memory, startup
Board Support Package

## Slide 22: Anatomy of a Board Support Package
ModusToolbox™ Board Support Package (BSP)
Device resource initialization Pins, Clocks, Power
Board dependent libraries and build recipes
Secure domain partition resources
Linker scripts and startup code
Peripheral configuration structures
Software aliases for hardware resources

## Slide 23: Directory structure of a Board Support Package
The config/GeneratedSource/ files are generated by Device Configurator from design.modus
You edit design.modus in the GUI; the .c/.h files are regenerated automatically

## Slide 24: Device Configurator flow
design.modus is binary XML — always edit via Device Configurator, never manually
Changes to pin assignments, clock speeds, or peripheral configs go here
When you switch BSPs, you get a different design.modus for the new board
Application Init
cybsp_init()
Auto-generated C files
config/GeneratedSource/
GUI based Configuration
Device Configurator (design.modus)
Configure pins, clocks, peripherals, and power modes with a GUI.
Stored in bsps/TARGET_APP_.../ config/design.modus
cycfg_pins.c / .h
  GPIO pin assignments and drive modes
cycfg_clocks.c / .h
  Clock tree configuration (PLL, dividers)
cycfg_peripherals.c / .h
  UART, SPI, I2C, Timer init structs
cycfg_system.c / .h
  Power modes, WDT, system-level config
One call initializes everything — pins, clocks, peripherals, power
All generated configuration is applied automatically at startup

## Slide 25: Demo BSP Walkthrough

## Slide 26: Workflows to develop and utilize a custom BSP

## Slide 27: Why Create a Custom BSP?
Infineon kit BSPs are a starting point…
  They provide a working configuration for the eval board and for the available code examples
  User prototyping on the Infineon kit will likely require BSP modifications — whether to leverage additional device capabilities or to match custom hardware.
Scenario | What Changes
Extending a kit BSP | Enable additional peripherals, change clock speeds, reconfigure pins to use more of the device's capabilities
Customer production board | Different pin assignments, no debug header, custom crystal, different memory layout
Multi-project sharing | Common BSP across a product line, maintained independently from application code

## Slide 28: Creating a custom BSP – modify existing BSP in place
(Optional) Copy the current BSP first if you want to preserve it
Is it possible to re-add a new BSP from Infineon GitHub (caution regarding BSP versions)
Change device (MPN), pins, clocks, peripherals as needed
Open BSP Assistant from Eclipse Quick Panel or VS Code ModusToolbox™ Assistant extension
This modifies the CURRENT BSP in the project — it does not create a new one
Save → Device Configurator regenerates configuration
Step 1:
Step 2:
Step 3:
Step 4:
Build and test
Use IDE build or make build → make program
Step 5:

## Slide 29: Creating a new custom BSP using standalone BSP Assistant
Launch BSP Assistant from ModusToolbox™ Dashboard (or Windows Start menu)
Select "Create New BSP based on..." an existing Infineon kit BSP or Device Part Number
Open Library Manager in the project
  If saved into bsps/: select and enable the new BSP as the active target
  If saved externally: browse to and add the BSP, then enable it
Save the new BSP to one of two locations:
  Directly into the project's bsps/ folder (e.g., bsps/TARGET_MY_CUSTOM_BOARD/)
  An external location (to be added to the project later)
Edit configuration using Device Configurator
Save → Device Configurator regenerates configuration
Step 1:
Step 2:
Step 3:
Step 4:
Build and test
Use IDE build or make build → make program
Step 5:

## Slide 30: Making Your custom BSP available to others
Project-local (simplest)
  BSP lives in bsp/ directory, committed with project
  Self-contained, no external dependencies
  Version controlled by the project’s own Git history
Shared via Git repo
  Commit custom BSP(s) to dedicated Git repo
  Team members clone the repo to local folder
  For new projects
    Open Project Creator and browse for local BSP folder
    Select folder and continue with application election
  For existing projects
    Use Library Manager to add / enable BSP
Method | How | Best For
Project-local | BSP lives in bsps/ inside the project | Single project, self-contained
Shared via Git repo | BSP(s) committed to a dedicated repo, cloned locally | Team-wide use, multiple projects, easy distribution
Manifest-published | BSP in its own Git repo, referenced via custom manifest | Organization-wide standard, integrated with Library Manager (power-user)

## Slide 31: Best practices for custom BSPs
Practice | Why
Always start from a kit BSP | Ensures correct startup, linker, and configurator files
Modify freely — the BSP is yours | BSPs were moved into the project specifically so users can customize them. The original Infineon BSP can always be restored via Library Manager
Use descriptive naming for custom boards | TARGET_MY_PRODUCT_V2 — makes it clear this targets specific hardware
Version your custom BSP | Use Git tags so projects can pin to a known-good BSP version
Document pin changes in Device Configurator | Use the User Notes feature (recent addition) to annotate pin assignments, clock choices, and design rationale directly in design.modus — stays with the configuration
Test with Device Configurator first | Validate pin/clock config before writing application code

## Slide 32: Demo / Exercise Create your own custom BSP

## Slide 33: Exercise - Create your own custom BSP
Step | Action | Expected Result
1 | Copy the kit BSP from your project into a new TARGET_MY_BOARD/ directory | New BSP directory appears in bsps/
2 | Switch to the new BSP: Library Manager (select MY_BOARD → Update) or edit Makefile TARGET=MY_BOARD → make getlibs | Makefile TARGET= updated, libs/mtb.mk regenerated
3 | Open Device Configurator on the new BSP | See the inherited kit configuration
4 | Change one pin assignment (e.g., move USER_LED to a different pin) | Config updates visually
5 | Save the configurator changes | GeneratedSource/ files regenerate

## Slide 34: Middleware integration with Library Manager and Makefiles

## Slide 35: Library Manager Overview
What it does:
View all middleware currently in your project
Add new middleware libraries
Update existing libraries to newer versions
Remove libraries you no longer need
How to launch:
Eclipse IDE: Tools → Library Manager (or Quick Panel)
VS Code: ModusToolbox™ Assistant extension → Application tab → Configure Middleware
Command line: make modlibs or make library-manager

## Slide 36: Shared libraries across workspace projects
One copy on disk, shared across all projects at that version
Multiple versions coexist: release-v1.8.0/ and release-v1.9.0/ side by side
libs/mtb.mk contains SEARCH_* paths that point the build system to mtb_shared/
Pin to release tags in .mtb files for reproducible builds

## Slide 37: Adding middleware to project
Step 04
Build system picks it up
Step 03
Project updated
Step 02
Click update in Library Manager
Step 01
Select library in Library Manager
.mtb file created (including dependencies) make getlibs performed Library source is added to workspace
Next make build automatically compiles the new library
No manual Makefile edits to “include library source”
Click "Add Library" in the Library Manager UI Select required middleware
Makefiles (libs/mtb.mk) updated to include middleware folders and search paths for mtb_shared

## Slide 38: Using Makefiles to integrate and configure middleware
Inclusion of middleware into the build system occurs automatically based on the Library Manager output (make getlibs)
Integration and configuration of middleware may require edits to the Makefile
  COMPONENTS
  DEFINES

## Slide 39: How do you know what COMPONENTS and DEFINES to add?
Location | What you'll find | How to access
Library README.md | Quick-start guide, required COMPONENTS and DEFINES, API overview, code snippets | Open mtb_shared/<library>/<version>/README.md in your IDE, or view on the library's GitHub repo
Library docs/ folder | Full API reference (HTML), configuration guide, migration notes | Open mtb_shared/<library>/<version>/docs/ typically contains generated HTML API docs
IDE quick links | Direct access to API documentation for libraries in your project | Eclipse: Quick Panel → Documentation section VS Code: ModusToolbox™ Assistant extension → Documentation links
Library GitHub repo | README (same as above), release notes, code examples list, issue tracker | Reference the library URL in the .mtb file or find it in Library Manager
Code examples | Working, tested projects that demonstrate the library in context | Links in the library README under "Code Examples" or "Related Resources"

## Slide 40: Practical workflow — when you add a new library
Add library via Library Manager → click Update
Open mtb_shared/<library>/<version>/README.md ← START HERE
README tells you:
  Required COMPONENTS (add to Makefile)
  Required DEFINES (add to Makefile)
  Required dependency libraries (added automatically via Library Manager)
  Initialization code to add to main.c
For deeper API details → open mtb_shared/<library>/<version>/docs/api_reference.html
For working examples → follow Code Example links in README

## Slide 41: Middleware summary and key takeaways
Concept | Key Point
Library Manager | GUI for managing .mtb pointer files — handles make getlibs automatically
README.md & docs/ | Every library ships its own docs — COMPONENTS, DEFINES, dependencies, API reference
COMPONENTS | Makefile variable that toggles optional library features (check library README)
DEFINES | Makefile preprocessor defines to configure library behavior (check library README)
mtb_shared | Shared library storage — one copy per version, shared across projects
Version pinning | Use release tags in .mtb files, not main branch

## Slide 42: Demo Library Manager and CMSIS-DSP COMPONENT

## Slide 43: Introduction to the upcoming ModusToolbox™ SDK

## Slide 44: How the development model is evolving
 | Current Model | SDK Model
Project creation | BSP → CE → download manifests → clone from GitHub | BSP → CE → SDK → copy from local install
Dependencies | .mtb pointers in deps/ Stored in mtb_shared/ via make getlibs | No .mtb, no deps/, no mtb_shared/ libraries in project libs/
Versioning | Each library versioned independently User verifies compatibility | All library versions locked to SDK version
Middleware | Shared, read-only in mtb_shared/ | Local to project, editable directly
Offline | GitHub required for every make getlibs | Fully offline after SDK install
Portability | Recipient must make getlibs to reconstruct | App is self-contained and shareable as-is

## Slide 45: What the SDK provides
ModusToolbox™
SDK
All supported boards, tested versions
BSPs
Middleware
Tools
PDL, Retarget-IO, Machine Learning, Motor Control, FreeRTOS, ...
Device Configurator, Library Manager, CAPSENSE Configurator, Build system...
Predictability — "I'm using SDK v1.2" tells support everything they need to know
Tested together — Infineon validates the full combination before release
Self-contained — applications include all middleware; no external mtb_shared/ dependency
Simpler upgrades — bump one SDK version instead of updating 15 libraries individually
Code Examples
Reference projects aligned specifically with included middleware
Documentation
Release notes, user guides

## Slide 46: What changes for you and your customers
What doesn't change:
  Makefile structure and build commands (make build, make program)
  Device Configurator workflow and BSP customization workflow
Workflow | Current | With SDK
Creating a project | BSP → CE → download manifests → clone from GitHub | BSP → CE → SDK → copy from local install
Project structure | deps/ + .mtb files libs/ = transitive pointers mtb_shared/ | deps/ and mtb_shared/ gone libs/ = real source bsps/ → bsp/
Library versions | Add, remove, update individually via Library Manager | Add/remove within SDK Version changes require SDK upgrade
Version control | Commit .mtb pointers mtb_shared/ not committed | Commit middleware source directly App is self-contained
Sharing | Recipient must make getlibs to reconstruct | App includes everything SDK needed only for tools
Middleware ownership | Shared in mtb_shared/ not typically edited | Local and editable in libs/ SDK detects changes on upgrade

## Slide 47: SDK summary and key takeaways
Point | Detail
SDK = curated bundle | BSPs + middleware + code examples + tools, tested as a set
One version number | Library versions locked to SDK; upgrade SDK to update libraries
Self-contained apps | No deps/, no mtb_shared/ — middleware source lives in project libs/, editable directly
Simplified workflow | BSP → Code Example → SDK; fully offline after install; no make getlibs
Current concepts apply | Makefiles, BSPs, COMPONENTS, Device Configurator all unchanged
Migration supported | Guided tooling to convert existing projects; both models coexist during transition

## Slide 48: Q&A

## Slide 49
Talk to your customers about how ModusToolbox™ can help them enhance their development experience.
Please download collateral and training materials now.

## Slide 50: Take a minute to share your thoughts! Your feedback is invaluable to us, and it plays a crucial role in helping us improve and deliver the best training experiences. Please open your IADT app and complete this session survey
Thank you for taking the time
to help us win together!